## Slide 1: Laboratory Secure SoC for the Internet-of-Things Second Introduction
Thomas Schamberger
24.04.2018
Institute for Security in Information Technology
Prof. Dr.-Ing. Georg Sigl

## Slide 2: Agenda
Network Review
IPv6
WSN with 6LowPAN
MQTT
  Securing the MQTT Connection
Lab Hardware/Software
  Tasks
Organization

## Slide 3
Network Review

## Slide 4: TCP/IP Layers
APPLICATION
TRANSPORT
NETWORK
LINK/PHYSICAL
Alice
Bob

## Slide 5: TCP/IP Layers: Application
APPLICATION
TRANSPORT
NETWORK
(Internet)
LINK
Data
Generate Data

## Slide 6: TCP/IP Layers: Transport
APPLICATION
TRANSPORT
Port (16 bits)
Data
TCP/UDP
Source Ports, Destination Ports
(0 to 65535)
Port

## Slide 7: TCP/IP Layers: Network
APPLICATION
TRANSPORT
NETWORK
(Internet)
LINK/PHYSICAL
IP
Data
Port
IP Adress
Source IP, Destination IP

## Slide 8: TCP/IP Layers: Link
APPLICATION
TRANSPORT
NETWORK
(Internet)
LINK/PHYSICAL
0 1 1 1 0 0 1 0
MAC
Media Access Control IEEE 802

## Slide 9: TCP: Transport
Connection: 3 way handshake
Start communication
Alice
Alice
Bob
SYN
SYN,ACK
ACK
DATA
DATA
FIN
ACK
ACK
FIN
DATA
Connection
End communication

## Slide 10: Comparison TCP/UDP
TCP | UDP
Connection oriented | Connectionless
Rearrangement of packet order | No reordering available
Acknowledgement of messages | Faster then TCP
Reliable | Less Overhead

## Slide 11: IP-Adresses
IPv4
        94.31.94.96
Example: Are those Hosts in the same network?
      192 . 168 . 0 . 1
      192 . 168 . 0 . 190
Routing
Same network
Gateway/Router

## Slide 12: TCP/IP Internet Protocol Suite
Breakdown of TCP/IP layers

## Slide 13
IPv6

## Slide 14: IPv6 - Overview
Addresses of size 128 bit compared to 32 bit for IPv4
Different notation:
    Trailing zeros can be eliminated:
    Zero groups can be substituted by “::”
2001:0db8:4004:0010:0000:0000:6543:0ffd
2001:db8:4004:10:0:0:6543:ffd
2001:db8:4004:10::6543:ffd
Network ID
Interface ID
64 bits
64 bits

## Slide 15: IPv6 - Prefixes
There are different types of addresses:
  Link-local addresses:
    Can only be used to communicate with hosts on the same network
    Start with FE80::
  Global addresses:
    Prefix given by router
    2001:4ca0:2fff:11::94

## Slide 16: IPv6 - Quiz
Which of the following are correct IPv6 addresses:
  2001:db8:A:B:C:D::1
  2001:db8:000A:B00::1:3:2:F
  2001:0db8::F:A::B
Notes: 1.) Correct
2.) Falsch (zu viele Adressen)
3.) Falsch zwei mal ::

## Slide 17
WSN with 6LoWPAN

## Slide 18: 6LoWPAN
IPv6 over Low-Power Wireless Personal Area Networks

## Slide 19: 6LoWPAN – Stack
Source: http://www.ti.com/lit/wp/swry013/swry013.pdf

## Slide 20: IEEE 802.15.4
Defines Physical and Data Link layer
2,4 GHz or Sub-1 GHz band
Designed for low-cost and ultra-low power design
Throughput is limited to 250 kbps
Frame length is limited to 127 bytes:
  Low packet and bit error rates
  Reduced power
Source: http://www.ti.com/lit/wp/swry013/swry013.pdf

## Slide 21: 6LoWPAN: IEEE 802.15.4
Adaption layer to enable the efficient transport of IPv6 packets over a 802.15.4
Protocol describes:
    Fragmentation/reassembly (RFC4944)
      IPv6 requires an MTU of 1280 bytes but 802.15.4 only has a frame length of 127 bytes
    Header compression methods (RFC4944,RFC6282,RFC7400)
      40 byte IPv6 header takes large part of packet
    Autoconfiguration (RFC4944)
http://www.9tut.com/ipv6-questions

## Slide 22: 6LoWPAN – Network Overview
Source: http://www.ti.com/lsds/ti_de/wireless-connectivity/6lowpan/overview.page

## Slide 23
MQTT

## Slide 24: MQTT Overview
A publish–subscribe based protocol used on top of the TCP protocol
Managed by a central entity called the MQTT-Broker
Messages are grouped under topics
Clients can subscribe / publish to certain topics of the broker
MQTT Client
B
MQTT Broker
MQTT Clients
Publish
Publish

## Slide 25: MQTT - Connect
B
CONNECT
CONNACK
Source: https://www.hivemq.com/blog/mqtt-essentials-part-3-client-broker-connection-establishment

## Slide 26: MQTT - Subscribe
MQTT Client
B
MQTT Broker
1.) SUBSCRIBE
4.) PUBLISH
2.) SUBACK
3.) PUBLISH
Source: https://www.hivemq.com/blog/mqtt-essentials-part-4-mqtt-publish-subscribe-unsubscribe

## Slide 27: MQTT - Publish
MQTT Client
B
MQTT Broker
Publish
Publish
https://www.hivemq.com/blog/mqtt-essentials-part-4-mqtt-publish-subscribe-unsubscribe

## Slide 28: MQTT - Example
B
MQTT Publisher
MQTT Broker
MQTT Subscriber
MQTT Subscriber
Publish:
Topic = pulse
Message = “100 bpm”
Subscribe to “pulse”
Publish: “100 bpm”
Subscribe to “pulse”
Publish: “100 bpm”

## Slide 29
Securing the MQTT Connection

## Slide 30: Problem
Authentication with MQTT is optional
Credentials transferred in plaintext with the connect packet
Solution: Use Transport Layer Security (TLS) to secure the whole TCP packet
TLS

## Slide 31: TLS (Transportation Layer Security)
Handshake: Algorithms and keys are negotiated
Record layer: Data is encrypted
Client HELLO
ACK
Server HELLO
ACK
SHARED KEY EXCHANGE
ENCRYPTED HANDSHAKE

## Slide 32: TLS (Transportation Layer Security)
Cryptographic protocols that provides communication security over a network
    Security: e.g. symmetric cryptography
    Authenticity: e.g. public-key cryptography
    Data integrity: e.g. MAC (message authentication code)
TLS cipher suites supports different methods for:
    Key exchange: RSA, PSK, ECDH-RSA, ...
    Data encryption: AES CCM, AES GCM, Camellia GCM, ...
    Data integrity: HMAC-MD5, HMAC-SHA1/SHA256, ….
Commonly used in securing web browsing, email, Internet, etc.

## Slide 33: Problem with Sensortag
The sensortag has not enough resources to use TLS
Alternatives have to be found
CAUTION:
If possible established cryptographic algorithms or techniques have to be used in practice. Use proven libraries like mbedTLS if possible!

## Slide 34: AES – Encryption of the payload
AES-128
  Input size = 128 bit
  Output size = 128 bit
  Key size = 128 bit
  10 Rounds
SubBytes
ShiftRows
MixColumns
AddRoundKey
AddRoundKey
SubBytes
ShiftRows
AddRoundKey
Rounds 1- 9
Round 0
Round 10

## Slide 35: AES – Encryption of the payload
What if someone manipulates the encrypted data??
Solution: Authenticated encryption with AES-GCM

## Slide 36: AES-GCM
Authenticated encryption with AES-128
IV has to be different for each encryption
Input:
  Plaintext (P)
  Additional authenticated data (A)
  Initialization Vector (IV)
AES-GCM
Output:
  Ciphertext (C)
  Authentication tag (T)

## Slide 37: GCM-Encryption

## Slide 38: GCM-GHASH

## Slide 39: GCM-Encryption

## Slide 40: GCM-GCTR

## Slide 41: MQTT Security
Mqtt-Header
Payload
AES-GCM
Message
Nonce
Ciphertext
AAD
Tag
IV

## Slide 42
Lab Hardware/Software

## Slide 43: Lab Hardware
Nodes consist of TI Sensortags
VM on Lab PC:
Acts as edge router
MQTT broker
Connected trough USB

## Slide 44: Overview – Edge router
Source: https://github.com/cetic/6lbr/wiki/6LBR-Modes

## Slide 45: Contiki OS
Operating system for the TI Sensortag
Provides the following features:
  Memory allocation
  Full IP networking
  6LoWPAN networking support with the Sensortag hardware
  TI drivers for the hardware of the sensortag:
    Sensors
    AES
    Random number generation
  Timers
  Use of protothreads for control flow

## Slide 46: Contiki - Example
Documentation:
https://github.com/contiki-os/contiki/wiki
http://contiki.sourceforge.net/docs/2.6/

## Slide 47: Conikti – Given application
You are given an application for the Sensortag
Consists of the following:
  Sensor values can be read from Contiki
  Features a http server that can be contacted from the edge router
    Change settings
    Show sensor values in HTML site
  MQTT-broker
  Library for Sensortag peripherals

## Slide 48
Tasks

## Slide 49: Part 1: Infrastructure setup + Clone of existing sensortag
What will be given:
  Contiki operating system with running MQTT client
  Edge router in Virtual machine
  Compiled program of sensortag with authentication credentials
  Makefile + Script for programming of the devices
  Sniffer binary that can be used together with wireshark
Your task:
  Analyse the connection packages with Wireshark to find out authentication credentials
  Use the found credentials to program a sensortag to act as a clone
After part 1 you are:
  Familiar with the code basis
  Know how to compile programs and flash them onto a sensortag
  Understanding the MQTT protocol
  Able to use wireshark to inspect messages
The running setup + clone sensortag has to be shown on the 15.05!

## Slide 50: Part 2: Secure communication
Mqtt-Header
Payload (Sensordata)
Pre-shared key
Use AES-GCM for authenticated encryption of the mqtt payload.

## Slide 51: Part2: Tasks
MQTT is already implemented in Sensortag application  Only change to payload function needed
Tasks for AES-GCM:
  Implementation of AES (Or usage of AES hardware on Sensortag)
  Implementation of RNG for the creation of the IV for GCM
    TRNG on Sensortag
    Implementation of PRNG
  Implementation of AES-GCM:
    Multiplication in GF(128)
    GHASH Function
    GCTR Function

## Slide 52
Organization

## Slide 53: Material on Gitlab
Lab material will be on Gitlab:
  Scripts to flash the sensortag
  Sensniff script to use with wireshark
  Contiki source
  Documentation of the Sensortag
  AES + GCM Standards
https://gitlab.lrz.de/

## Slide 54
Organizational Matters: Important Dates
54
Lectures:
  Presentations / Exam:
Date | Time | Place | Description
10.04.2018 | 09:45 am – 11:15 pm | N1005 | Introductory lecture
24.04.2018 | 09:45 am – 11:15 pm | N1005 | MQTT, Lab Hardware, Networking basics
Date | Time | Place | Description
15.05.2018 | 9:30 am – 12:00 pm | N1005 | Setup presentation
26.06.2018 | 9:00 am – 12:00 pm | N1005 | Final presentation
TBA | TBA | N1005 | Oral exam
Notes: 54

## Slide 55: Tutor hours
 | Monday | Tuesday | Wednesday | Thursday | Friday
10.00 – 13.00 |  |  |  |  | 
14.00 – 17.00 |  | X |  |  | 

## Slide 56
Lab Hardware / Groups